## Slide 1: Update on Newton BERDO Michael Gevelber
Issues:
Overview
Case Study Overview: Apts at xxx Lexington St
Question: should electricity emissions be part of N-BERDO
Many slides taken from Philip Eash-Gates, PE, CEM, Principal Associate
Synapse Energy Economics, Inc.

## Slide 2: Newtib BEERDO Building Counts, Area, Emissions
Tier | Description | Count of Buildings | Total GFA (Msq ft)/ emissions %
1 | Non-residential, ≥100,000 sq ft | 47 | 8.6M / 42%
2 | Non-residential, 50,000–99,999 sq ft | 71 | 5 M / 23%
3 | Non-residential, 35,000–49,999 sq ft Residential, ≥50,000 sq ft | 68 17 | 2.9M / 13% 2.1M / 6%
4 | Non-residential, 20,000–34,999 sq ft | 109 | 2.9M / 13%
5 | Residential, 20,000–49,999 sq ft | 44 | 1.2M /3 %
Total | All covered buildings | 356 | 22,724,984

## Slide 3: 206 Newton Building Owners
80 percent of owners have one covered building
4 percent of owners have non-residential condos
7 owners have 5 or more covered buildings:
Property Owner | Number of Covered Buildings
Trustees of Boston College | 40
City of Newton | 34
Lasell University | 20
Roman Catholic Archdiocese of Boston | 7
Chestnut Hill Shopping Center | 6
Newton Housing Authority | 5
Donato D. Capasso Trust | 5

## Slide 4: Proposed Newton BERDO Timeline
Notes: Philip

## Slide 5: Newton Emission Standard (v1.0)
Building typology | Emission standards (kgCO2e/SF) |  |  |  |  | 
Year | Period 1 | Period 2 | Period 3 | Period 4 | Period 5 | Period 6 2050–
Assembly | 12.5 | 7.7 | 5.8 | 3.4 | 1.6 | 0.0
College/University | 18.4 | 10.5 | 6.9 | 3.9 | 1.9 | 0.0
Education | 4.9 | 3.8 | 2.9 | 1.9 | 0.9 | 0.0
Food Sales & Service | 34.4 | 18.2 | 13.7 | 8.3 | 4.2 | 0.0
Healthcare | 18.1 | 14.6 | 11.6 | 7.5 | 3.7 | 0.0
Lodging | 8.1 | 5.8 | 4.4 | 2.8 | 1.4 | 0.0
Manufacturing/Industrial | 27.8 | 23.2 | 18.7 | 11.6 | 5.1 | 0.0
Multifamily housing (residential buildings, RB) | 6.0 | 4.1 | 3.0 | 1.8 | 0.9 | 0.0
Office | 19.5 | 6.0 | 4.3 | 2.5 | 1.2 | 0.0
Retail | 14.6 | 9.2 | 6.0 | 2.7 | 1.2 | 0.0
Services | 13.2 | 7.6 | 5.5 | 3.4 | 1.7 | 0.0
Storage | 13.6 | 6.9 | 4.3 | 2.2 | 0.8 | 0.0
Technology/Science | 24.8 | 19.3 | 14.6 | 8.4 | 3.9 | 0.0
Individual compliance schedule (percent relative to baseline year) | 86.7% | 73.3% | 60% | 40% | 20% | 0%
Notes: Philip

## Slide 6: DRAFT Newton Emission Standard, Boston & PRC
Notes: Explain steps for each city (Boston starts 2025, Cambridge 2026 (large) and 2030 (small), Newton 2026 for tier 1 (phase other tiers in gradually)
Cambridge allows use of carbon credits: 40% of baseline emissions in period 3 (2035-2039), less in other periods

## Slide 7: Case Study: Apts at 181 Lexington.
30-unit apartment building. Constructed in 1970 gross floor area of 24,570 square

## Slide 8: Energy/Emissions Breakdown (estimate)
Energy source | Energy use | Energy use intensity | Emissions | Emissions intensity
 | kBtu | kBtu/sqft | kg CO2e | kg CO2e/sqft
Electricity | 293,000 | 11.9 | 9,000 | 0.37
Natural gas | 1,438,000 | 58.5 | 76,000 | 3.09
Total | 1,731,000 | 70.4 | 85,000 | 3.46
Table 1. Energy use and emissions at 181 Lexington Street, 2022
Over 2022, 16–20 units participated in Newton Power Choice.
All participants enrolled at the Standard level, 84 percent renewable power

## Slide 9: Natural Gas use:
3.1 kg CO2/sqft: 1.9 is for heating
38% of natural gas use is for DHW & Dryers. (1.2 kgCO2/sq ft)

## Slide 10: Case study observations
3.46 kilograms of carbon dioxide equivalent (kgCO2e) per square foot. .36 kgCO2/sq ft from electricity
3.1 kgCO2/sqft is from Natural Gas combustion. 38% from DHW & Dryers. (1.2 kgCO2/sq ft)
1.9 kgCO2/sqft is for heat
Proposed maximum emissions limits for apartment buildings less than 50,000 square feet are 4.8 kgCO2e per square foot, beginning in 2030.
By 2038, the target would decrease to 2.6 kgCO2e per square foot Buildings. 2042-45 is 1.6
Options for compliance: don’t need to replace all natural gas at once. DHW, Dryers, could
Use hybrid (natural gas-heat pump for heating hot water (50% of capacity)

## Slide 11: Should we include electricity in Newton Berdo?
Massachusetts will get to nearly 90% by 2030.
If so, why should Newton BERDO include electricity emissions? Focus on the hard things that require large CapX

## Slide 12: EIA data of MA Elec Generation: how replace 74% of gen capacity in 7 years & whats it going to cost???
Utility-Scale Net Electricity Generation (share of total) | Massachusetts | U.S. Average |  | Period | 
Petroleum-Fired | 0.1 % | 0.3 % |  | Jun-23 | find more
Natural Gas-Fired | 73.7 % | 45.3 % |  | Jun-23 | find more
Coal-Fired | 0.0 % | 16.2 % |  | Jun-23 | find more
Nuclear | 0.0 % | 18.2 % |  | Jun-23 | find more
Renewables | 23.4 % | 19.6 % |  | Jun-23 |