## Slide 1: Riverside Station Peer Review Findings Summary Traffic Impact and Access Study (TIAS) 2/12 Report and Subsequent Revisions
Prepared for: City of Newton, Massachusetts
By: Fay, Spofford & Thorndike
December 18, 2012

## Slide 2: Peer Review Findings Summary - Overview
TIAS generally well prepared, thorough, most assumptions reasonable
TIAS trip generation, regional Trip Distribution, and Existing and No-Build analyses acceptable
Grove Street route choice traffic impacts identified in the TIAS was an issue that was addressed
Roundabouts with Options B-2 or A are expected operate better than and with fewer crashes than the No-Build Exit 22 and reduce ramp delays compared to the No-Build
Site parking still needs further clarification. Peak parking demands will be satisfied sufficiently assuming a sound shared parking arrangement is created
Prepared for: City of Newton

## Slide 3: TIAS Study Area Key Finding: Adequate
Prepared for: City of Newton

## Slide 4: Trip Distribution Adjustment
Key Finding: Regional Distribution adequate, local Grove Street distribution needed adjustment
Original TIAS projected
a maximum of 80-85
(14-16%) of
site-generated
trips/hour use Grove/
Auburn/Washington
corridor to and from
I-90 east. Greater use
of this corridor expected
Redistribution at measured 29% level represents 65 to 80 additional peak hour trips over the 80-85 assumed & would still be consistent with TIAS’s regional distribution pattern.
Applicant re-distributed and checked impacts to see if additional mitigation is warranted; non-structural preferred
Signal timing adjustments required at three locations.
Concurrently reduces C-D Road and Exit 22 ramp volumes by up to 65 to 80 trips per hour
Prepared for: City of Newton
Riverside

## Slide 5: Study Area Comparisons 2022 AM Peak Hour Mitigated Build vs. No-Build LOS’s W/Redistribution
Legend
LOS A-C
LOS D
LOS E
LOS F
Mitigated
Build
No-Build
Prepared for: City of Newton
NM – No Mitigation Proposed
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM

## Slide 6: Study Area Comparisons 2022 PM Peak Hour Mitigated Build vs. No-Build LOS’s W/Redistribution
Legend
LOS A-C
LOS D
LOS E
LOS F
Mitigated
Build
No-Build
Prepared for: City of Newton
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM
NM – No Mitigation Proposed
NM

## Slide 7: Options B-2 and A – Key Difference
Prepared for: City of Newton
Option B-2
Option A

## Slide 8: Peer Review Findings Summary - Options
Option B-2 has potential sight line/ramp conflicts issues but results in best east roundabout traffic operations and slightly better operations on Grove Street between Exit 22 and MBTA Site Drive
Option A is best from an overall traffic safety perspective
Compared to the No-Build, Option B-2 and A both reduce traffic volumes on Grove Street between the T entrance and Exit 22 – Option B-2 by nearly 2,300 vpd; and Option A by 700 vpd
Refinements to Options A or B-2 should be made to accommodate pedestrians and bikes better during design
The MBTA Site Drive approach to Grove Street should be two lanes to accommodate peak queuing demands
Prepared for: City of Newton

## Slide 9: Peak Hour Grove Street Traffic w/North Re-distribution
Chart: 
| AM | PM | AM | PM | AM | PM | AM | PM | AM | PM | 2012 | 2022 No-Build | 2022 Build | 2022 Mitigated Build Option A | 2022 Mitigated Build Option B-2
Grove Street south of MBTA | 1445 | 1520 | 1515 | 1590 | 1870 | 1990 | 1380 | 1580 | 1285 | 1350
Grove Street north of MBTA | 1230 | 1265 | 1285 | 1320 | 1425 | 1490 | 1425 | 1490 | 1425 | 1490
N

## Slide 10: Daily Grove Street Traffic w/North Re-distribution
Prepared for: City of Newton
Chart: 
| NO-BUILD | Option A Difference | Option B-2 Difference
Grove Street south of MBTA | 15111.3491 | -705.683 | -2287.3862
Grove Street north of MBTA | 12677.9595 | 1508.7015 | 1508.7015
N

## Slide 11: Buildings/Parking Overview
Existing
  Riverside Intermodal facility with Green Line/bus service and 963 surface commuter parking spaces
Future Development
  Office space – 225,000 gsf
  290 apartments – 320,000 gsf
  Retail space – 15,000 gsf
  Community space – 8,000 gsf
Future Parking
  Total 2014 spaces – net increase of 1, 051 spaces
  MBTA Commuter Spaces– 1,005 spaces
  Development Spaces – 1,009 spaces
      Offices – 563 spaces (2.5/1,000 gsf)
      Apartments – 435 spaces (1.5/unit)
      Surface – 11 spaces (Residential/retail building short term)
Prepared for: City of Newton

## Slide 12
2,014 total spaces; 1,009 private/free? – 1,005 public (MBTA)/pay
From 46-232 spaces in MBTA garage may need to accommodate non-commuter site users
How much non-commuter users will pay for site parking at MBTA is an issue, must be same rate for all users
Prepared for: City of Newton
Shared Parking Review

## Slide 13
Shared Parking Potential
by Type of Use
12M 12N 12M
12M 12N 12M
12M 12N 12M
Retail
Office
Apartments
20%
100%
80%
60%
40%
0%
20%
100%
80%
60%
40%
0%
20%
100%
80%
60%
40%
0%
Prepared for: City of Newton
Shared parking need
Shared parking potential spaces

## Slide 14: Shared Parking Conclusions
With clarifications, shared parking strategy as presented should reduce traffic demands
Vast majority of typical weekdays, the MBTA should be able to satisfy its commuter parking demands
From 46-232 spaces in MBTA garage may need to accommodate non-commuter site users
Community space parking should be worked out with Building A
Prepared for: City of Newton

## Slide 15: Trip Generation
Key finding: Adequate
Total New Trips:
  Daily – 5,088 (2,544 in and out)
  AM Peak Hour – 496 (356 in and 140 out)
  PM Peak Hour – 575 (198 in and 377 out)
  Community building trip generation assumed as office space
Assumes:
  Office –365 AM / 321 PM Peak Hour New vehicle trips
  Retail– 39 AM/139 PM Peak Hour New vehicle trips
  Residential– 104 AM/115 PM New vehicle trips
  MBTA intermodal facility - ‘neutral’ (i.e., ‘0’ New) generator depends on funding/operations service policies
  Fewer than 3 vehicles on average per minute estimated added to Grove Street to and from the north during peak hours
Prepared for: City of Newton

## Slide 16: Grove Street: Looking North the MBTA Entrance
Prepared for: City of Newton

## Slide 17: Key Finding: Option B-2 has superior vehicle traffic operations but a potential sight line & conflicts safety issue not associated with Option A
Prepared for: City of Newton

## Slide 18: Grove Street roundabouts
Far lower crash experience expected than with signals or the current interchange configuration
Operate best with Option B-2, acceptably with Option A
Consider focusing most Exit 22 pedestrian crossings to the north side of interchange roundabouts where best environment can be created
Prepared for: City of Newton

## Slide 19: Potential Grove Street Pedestrian/Bike Enhancements
Consider eliminating free right and maximizing deflection; change SB I-95 merge to Grove Street to yield to crossing traffic & bikes & focus pedestrian crossings on north side of the interchange
2 Buffer bridge bike
lane and one create crossing for bus stop users at 1 lane roundabout crossing
Consider maximizing deflection for NB merge to enhance bike & Grove Street NB merges; no ‘free’ right turn movements
Consider using raised medians with deflection between the two Grove Street lanes for1-lane pedestrian crossings at a time
5 Consider 5-foot bike lanes rather than 4-foot bike accommodations to new T entrance
Prepared for: City of Newton
3
2
1
5
4

## Slide 20: Grove Street – West Roundabout Measures to Consider
Grove Street
Pierrepoint Road
Asheville
Road
1 - 2

## Slide 21: Grove Street – East Roundabout Consider Modified Pedestrian Crossing
Grove Street
3 - 4

## Slide 22: Grove Street – 5-foot bike lane vs. 4-foot accommodation
Prepared for: City of Newton
Use 11’ lanes rather than 12’ lanes for 5’ bike lanes
Grove Street
5

## Slide 23: I-95 Northbound C-D Road Looking north to future site ramps vicinity
Prepared for: City of Newton
Vicinity of proposed left turn out
Potential snow bank area that could impede winter sight lines inside horizontal curve

## Slide 24
Grove Street:
Looking south to MBTA Entrance
Prepared for: City of Newton

## Slide 25: Key Traffic Peer Review Findings: Mitigation
  Option A has better traffic and pedestrian safety features, but Option B-2 provides better traffic operations. If Option B-2 sight line/CD Road conflicts issue cannot be resolved, FST prefers Option A for safety reasons – FHWA will ultimately decide
  Necessary Grove Street physical modifications are similar with Options A and B-2 access options
  Grove Street traffic projection re-distribution was performed acceptably; implementation of additional mitigation measures is appropriate for those locations that worsen traffic operations compared to the No-Build Alternative
  Proposed TDM measures are reasonable, but need to be continuously applied/reinforced in the context of post implementation counts
  Consider Grove Street alternate measures from TIAS for pedestrian/bicycle/environmental enhancements as they pertain to roundabouts and the T entrance traffic signal
  Post-implementation measures are appropriate and should include a review of pre- and post-implementation neighborhood parking assessment as well as follow up counts.
Prepared for: City of Newton

## Slide 26: Key Peer Review Findings: Responsiveness of TIAS to Expressed City and Neighborhood Concerns
Reduces build from DEIR as requested
Itemized TDM measures as requested
Analyzed alternate site distribution pattern to and from I-90 to the east was evaluated and
Addresses Fenway event day traffic volumes, but not event day parking demands
Prepared for: City of Newton

## Slide 27: Based on Peer Review Findings, the Applicant:
    Redistributed peak hour traffic on Grove Street corridor by assuming a maximum of approximately 29% of total site generated traffic will travel to and from the north vs. 14-16% as presented in the TIAS and addressed mitigation
    Should commit that site-generated volumes on Grove Street corridor will not exceed projected TIAS volumes by more than 10% based on future count program and maximize site TDM measures.
    Needs to confirm retail/community building parking assumptions
Prepared for: City of Newton

## Slide 28: - Thanks Questions?
Prepared for: City of Newton