## Slide 1
The Dunstan Residences
West Newton Redevelopment
Transportation
Peer Review
City of Newton
Newton City Hall
June 28, 2021

## Slide 2
Peer Review Presenter
Jeff Maxtutis, Project Manager, Transportation Planner, BETA Group, Inc.

## Slide 3
Peer Review Process
Reviewed:
  Transportation Impact and Access Study – April 2021, VHB, Inc.
  Site Plans – April 8, 2021, VHB, Inc.
  Program Modification Trip Generation Memo – June 3, 2021, VHB, Inc.
Focus of review is on proposed Building #3
Presentation on outstanding comments

## Slide 4
Peer Review Process
Review included:
  Traffic data/analysis
  Pedestrian & Bicycle
  Transit
  Parking
  Internal Circulation
  Loading & curbside activity
  Transportation Demand Management (TDM)
  Consistency with Zoning and Newton Street Design Guide
Overall, the study met state and industry professional practice standards

## Slide 5
Project Program Changes
Proposed Changes in Building Program
Land Use | Approved Building Programa | April 2021 Updated Building Program | Change in Building Program
Residential | 234 units | 302 units | +68 units
Retail | 8,318 sf | 5,821 sf | -3,823 sf
Parking | 294 spaces | 338 spaces | +44 spaces
a Building Program approved in July 2020. |  |  | 

## Slide 6
Traffic

## Slide 7
Trip Generation Changes
Net New Project-Generated Trips | Weekday AM Peak Hour | Weekday PM Peak Hour | Saturday Midday Peak Hour
2020 Building Program | 167 | 82 | 53
Revised Building Program | 181 | 88 | 56
Difference | +14 | +6 | +3
Net New Vehicle Trips

## Slide 8
Traffic
Proposed Signal Timing Adjustments
  Washington Street/Prospect Street – Weekday Evening
  Washington Street/I-90 Eastbound On-Ramp – Weekday Evening
  Washington Street/Elm Street – Weekday Morning
  Washington Street/Lowell Avenue – Weekday Evening
  Washington Street/Walnut Street – Weekday Morning
  Watertown Street/Albemarle Street Southbound – Weekday Morning
  Watertown Street/Albemarle Street Northbound – Weekday Evening
  Provide Signal Timing adjustments for both the AM and PM peak periods for the seven intersections listed above and the intersection of Washington Street and Auburn Street which experiences an overall LOS F during the weekday evening peak.

## Slide 9
Retail Sensitivity Analysis Conditions
June 21, 2021 Memorandum by Applicant
Proposed increase in retail from 5,821 SF to 7,771 SF (+1,950 SF)
No more than 8 additional vehicle trips during peak hours
No significant impact

## Slide 10
Parking, Access, Circulation & Loading

## Slide 11
Project Parking
Project Element | Garage Spaces | Surface Spaces | Total
302 Residential Units | 302 (70 Building 3) | 0 | 302
Commercial and Residential Visitor | 20 | 16 | 36
Total | 322 | 16 | 338
Project Parking Summary

## Slide 12
Project Parking
Proposed 1.0 space per dwelling unit consistent with MBTA/MassDOT TOD guidelines and MAPC Metro Boston Perfect Fit Parking Initiative recommendations
Commercial Use: 113 parking spaces required per Newton Zoning Ordinance; 36 spaces proposed
Waiver of 77 spaces required, Applicant to update with additional 1,950 SF retail

## Slide 13
Project Parking
Need additional information on parking:
  Will 36 spaces for commercial use be shared with residential visitor use? Where, when and how?
  Will proposed increase in retail space by 1,950 SF require additional parking spaces?
  Will 16 parking spaces on Kempton Place be available for both retail and visitor use?
  Need to designate one of the spaces as handicapped parking.

## Slide 14
Parking
Provide dimensions and number of Compact parking spaces
Dimensional waivers required for:
  Parking aisle width of 22 feet (24 required)
  Parking stalls are 18 feet long (19 feet required)

## Slide 15
Site Access, Circulation, Loading
How and where will loading and deliveries be handled for Building 3 from both Kempton Place and Washington Street?

## Slide 16
Pedestrians, Bicycles, and TDM

## Slide 17
Pedestrians and Bicyclists
  Provide detectable warning panels across project driveways on Dunstan Street and Kempton Place
  Confirm number of bicycle parking spaces in garages and on-street
  Applicant should construct the sidewalk on the north side of Washington St. along project frontage with bicycle facilities consistent with Washington Street Vision as directed by the City Engineer

## Slide 18
Potential TDM Mitigation
Transportation Demand Management (TDM) Program Elements
  TDM Coordinator
  Rideshare options
  Information center
  Hosting events
  Monitor TDM effectiveness through surveys and counts
  Report results to City
  Indoor/outdoor bike parking
  Bike-sharing
  EV charging and parking
  Unbundling parking costs from leases

## Slide 19
Potential TDM Mitigation
Additional TDM Measures to Consider:
  Will car-sharing be provided in Building 3?
  Is a public transportation reimbursement included in the TDM plan for Building 3 residents?
  Are bike racks proposed on Washington Street along the Building 3 frontage?
  Will a bike share station be provided?
  How many EV charging stations will be provided in Building 3? ..

## Slide 20
Thank You